## Slide 1: PROJECT ON CNC MACHINES
Notes: <number>
Click to add notes

## Slide 2: INDEX
DEVELOPMENT OF CNC MACHINES
CNC SYSTEM
PROGRAMMABLE LOGIC CONTROLER
SERVO DRIVES
CNC RETROFITTING
MAINTENANCE MANAGEMENT

## Slide 3: DEVELOPMENT OF CNC MACHINES
EVOLUTION OF THE CNC MACHINES
CNC MACHINES DEVELOPMENTS
BENEFITS OF CNC MACHINES

## Slide 4: EVOLUTION OF THE CNC MACHINES
The first CNC Machine was built in 1949 at MIT ,USA for manufacturing of the Air Craft components having intricate profiles using electron tubes & core memory.
The technology advancement from the Tube technology to the open architecture system has enabled to revolutionize the manufacturing processes.

## Slide 5: CNC MACHINES DEVELOPMENTS
VERTICAL MACHINING CENTRE (VMC)
TURRET MACHINING CENTRE (TMC)
HORIZONTAL MACHINING CENTRE (HMC)
UNIVERSAL MACHINING CENTRE (UMC)
CNC TURRET PUNCH PRESS
CNC BENDING MACHINE
CNC UNIVERSAL GRINDING MACHINE
CNC GEAR CUTTING MACHINE

## Slide 6: BENEFITS OF CNC MACHINES
INCREASED FLEXIBILITY.
IMPROVED QUALITY.
REDUCED LEAD-TIME.
HIGHER PRODUCTIVITY.
ECONOMICAL BATCH PRODUCTION.
REDUCED CYCLE-TIME.
REDUCED SCRAP GENERATION.

## Slide 7: CNC SYSTEM
INTRODUCTION
CNC SYSTEM
CLOSE LOOP SYSTEM
OPEN LOOP SYSTEM
CNC CONTROLLER
CNC SYSTEM BLOCK DIAGRAM
MODES OF CNC M/C OPERATION
CNC MACHINES COORDINATES
ZERO OFFSET
CNC CONTROLLER OPEARTING AREAS
BENEFITS OF CNC MACHINES

## Slide 8: INTRODUCTION
CNC controllers are the heart of a machine or process. They provide control information used to produce parts. CNC controllers range in capability from simple point-to-point linear control to highly complex algorithms that involve multiple axes control. CNC controllers can be used to control various types of machine shop equipment. These include horizontal mills, vertical mills, lathes and turning centers, grinders, electro discharge machines (EDM), welding machines, Flame Cutting machines ,Press machines and inspection machines. The number of axes controlled by CNC controllers can range anywhere from one to five, with some CNC controllers configured to control greater than six axes. Mounting types for CNC controllers include board, stand alone, desktop, pendant, pedestal, and rack mount. Some units may have integral displays, touch screen displays, and keypads for control and programming.
Industrial communications options for CNC controllers include ARCNet, CANBus, ControlNET, Data Highway Plus, DeviceNet, Ethernet 10/100 Base-T, parallel, PROFIBUS, SERCOS, Universal Serial Bus (USB), serial (RS232, RS422, RS485), and web-enabled. Communications language choices include bitmap, conversational, DXF file, G/M codes, Hewlett Packard graphics language, and ladder logic. A bit map (often spelled "bitmap") defines a display space and the color for each pixel or "bit" in the display space. Conversational language is a higher level, easy to learn programming tool. It performs the same functions as the standard G-code commands. Drawing eXchange Format (DXF) file that was created as a standard to freely exchange 2 and 3 dimensional drawings between different CAD programs. It basically represents a shape as a wire frame mesh of x, y, z coordinates. G-code is the programming language for the Computer Numerically Controlled (CNC) machine tools that can be downloaded to the controller to operate the machine. M-code is the standard machine tool codes that are normally used to switch on the spindle, coolant or auxiliary devices.
Notes: <number>
  How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
  Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 9: CNC SYSTEM
CNC stands for Computer Numerical Control and has been around since the early 1970's. Prior to this, it was called NC, for Numerical Control .CNC controller are able to execute binary coded commands. The control code for a machine contains positioning as well as switching information. Positioning information is intended to position the workpiece or else the tool .Switching information controls the machines servo components. The coded instructions are entered manually at the control as well as DNC (Distributed Network Controller).
Measuring system record when the position of the workpiece or tool indicated on the part program has been reached. Function such as lubrication , coolant on/ off and workpiece clamping are activated using PLC (Programmable Logic Controller ) through relays & contactor at electrical panel.
CNC controllers have several choices for operation. These include polar coordinate command, cutter compensation, linear and circular interpolation, stored pitch error, helical interpolation, canned cycles, rigid tapping, and auto-scaling. Polar coordinate command is a numerical control system in which all the coordinates are referred to a certain pole. The position is defined by the polar radius and polar angle. Cutter compensation is the distance you want the CNC control to offset for the tool radius away from the programmed path. Linear and circular interpolation is the programmed path of the machine, which appears to be straight or curved, but is actually a series of very small steps along that path. Machine precision can be remarkably improved through such features as stored pitch error compensation, which corrects for lead screw pitch error and other mechanical positioning errors. Helical interpolation is a technique used to make large diameter holes in workpieces. It allows for high metal removal rates with a minimum of tool wear. There are machine routines like drilling, deep drilling, reaming, tapping, boring, etc. that involve a series of machine operations but are specified by a single G-code with appropriate parameters. Rigid tapping is a CNC tapping feature where the tap is fed into the work piece at the precise rate needed for a perfect tapped hole. It also needs to retract at the same precise rate otherwise it will shave the hole and create an out of spec tapped hole. Auto scaling translates the parameters of the CNC program to fit the work piece.
Notes: <number>
Example objectives
At the end of this lesson, you will be able to:
  Save files to the team Web server.
  Move files to different locations on the team Web server.
  Share files on the team Web server.

## Slide 10: CNC MACHINE TOOL (CLOSE LOOP SYSTEM)
SERVO
DRIVE
SERVO
MOTOR
S
P
I
N
D
L
E
TABLE
D N C LINK
TAPE READER
OTHER DEVICES
MACHINE ELEMENTS
DISPLAY UNIT
INPUT/OUTPUT
KEYBOARD
FLOPPY DISC / CD
BALL
SCREW
ENCODER
JOB
TACHO / POSITION
SENSOR
VELOCITY
FEEDBACK
POSITIONAL FEEDBACK
PLC
NC
CNC
I / P
O /P

## Slide 11: CNC MACHINE TOOL (OPEN LOOP SYSTEM)
SERVO
DRIVE
SERVO
MOTOR
S
P
I
N
D
L
E
TABLE
D N C LINK
TAPE READER
OTHER DEVICES
MACHINE ELEMENTS
DISPLAY UNIT
INPUT/OUTPUT
KEYBOARD
FLOPPY DISC / CD
BALL
SCREW
JOB
TACHO / POSITION
SENSOR
VELOCITY
FEEDBACK
PLC
NC
CNC
I / P
O /P

## Slide 12: CNC CONTROLLER
Electrically, a CNC Machine consists of a multi-axis servo drive, spindle (cutting) drive, one or more controllers, power supplies, and safety circuits. On larger systems, a programmable logic controller (PLC) may be used to handle auxiliary functions such as water cooling and lubrication functions ATC (Automatic Tool Changer) system, APC (Automatic Pallet Changer) system.
CNC Controller consist of various electronic cards such as Memory Board, NC-PLC communication Board, Input-Output Board, Video Board, PLC-CPU board, MCP(Machine control Panel), OCP (Operator Control Panel), Display unit etc.
In CNC System Part program is feed through manual or through program transfer device like digitek instrument & DNC (Distributed Network Controller) system. This part program stored in RAM memory of CNC controller. When machine is work in automatic mode the part program is called. Part program commands are executed by NC controller and give signal to Servo-drives, PLC etc.
In above CNC system block diagram commands are generated by CNC controller fed to Servo drive for axis movement. Servo drive generate the electrical power to move the servo motor for axes movements. In Servo loop the Tacho-generator which is coupled with servo motor give the velocity feedback signal to Servo drive .This system is known as velocity feedback system. For positioning of axis the encoder or Linear Scale-Transducer give positional feedback system to CNC controller. Apart from the positional command spindle CW/CCW, coolant ON/OFF, Tool change, Feed , G codes are executed by CNC controller & give signal to PLCs.
Notes: <number>
Example objectives
At the end of this lesson, you will be able to:
  Save files to the team Web server.
  Move files to different locations on the team Web server.
  Share files on the team Web server.

## Slide 13: TYPE OF CNC CONTROLLER
Siemens Sinumerik controller 8T, 810GA3,
840C, 840D, 802D, 810D
HMT Hinumerik Controller, 3100M,2000V2
Heidenhain TNC135, TNC415
Fanuc Controller Fanuc 6M, 16M,18M, Fanuc0, Fanuc0I

## Slide 14: CNC SYSTEM BLOCK DIAGRAM
MAIN
PROCESSOR
MEMORY
SYSTEM
SOFTWARE
PROGRAM
MACHINE
INTERFACE
P L C
DRIVE
MACHINE
INPUTS
~ M D I
~ PAPER TAPE
~ MAGNETIC TAPE
~ REMOTE LINK
~ D N C LINK
~ FLOPPY DISC / CD
OUTPUTS
~ DISPLAY UNIT
~ REMOTE LINK
~ D N C LINK
~ FLOPPY DISC / CD

## Slide 15: MODES OF CNC M/C OPERATION
CNC machine operates in different mode like JOG,MDI, AUTO, Increment mode 1, 10, 100, 1000, 10000 micron, REF, Data input / output mode, Repositioning mode .These all mode are to be selected from Machine Control Panel
JOG Mode: In this mode machine is operated in manually. In JOG mode machine moves in respective direction of axis when key is pressed. This mode is normally use for machine setting. when switch is not pressed machine can not move. Axis feed can be change by feed override switch.
REF Mode: In this mode machine is referenced before operating the CNC machine in Automatic mode (programming mode), machine needed to be referenced. Reference means machine zero position. It is very necessary to reference M/c because during power off CNC system loose its positional value.
AUTO Mode: In automatic mode, individual NC traversing programs are processed. The axes cannot be traversed by means of the direction keys. In this mode machine works in part programs .Part program is program of particular job. part program contains various codes like that the numeric value of axis position ,tool command, spindle rotation , spindle speed, coolant on/off, G-codes, M-codes, T-codes etc.
INCR 1,10,100,1000,10000 Mode: In this mode machine move in 1, 10, 100 , 1000, 10000 microns when switch is pressed with respect to direction of axis. This mode is normally is used for fine setting of jobs.
MDI Mode: This mode in known as manual data input mode .In MDI mode machine execute the program block.MDI mode normally is for small program.like Tool change Pallet change ,Spindle ON /OFF etc.
Notes: <number>
Example objectives
At the end of this lesson, you will be able to:
  Save files to the team Web server.
  Move files to different locations on the team Web server.
  Share files on the team Web server.

## Slide 16: CNC MACHINES COORDINATES
Coordinate systems: Right–handed, rectangular coordinate systems are used for machine tools. Such systems describe the movements on the machine as a relative motion between tool and work piece.
Machine Coordinate System( MCS) :The orientation of the coordinate system on the machine tool depends on the particular machine type. It can be turned to various positions. The origin of the coordinate system is the machine zero. All axes are in zero position at this point. This point is merely a reference point determined by the machine manufacturer. It need not to be approachable.

## Slide 17: CNC MACHINES COORDINATES
WORKPEICE COORDINATE SYSTEM (WCS): The workpiece coordinate system described is also used to describe the geometry of a workpiece in the workpiece program. The workpiece zero can be freely selected by the programmer. The programmer need not know the real movement conditions on the machine, i.e. whether the workpiece or the tool moves; this can be different in the individual axes. The definition of the directions is based on the assumption that the workpiece does not move and the tool moves.

## Slide 18: ZERO OFFSET
ZERO OFFSET: The actual values are referred to the machine zero after a reference point approach. The machining program of the workpiece refers to the workpiece zero. Machine zero and workpiece zero need not be identical. Depending on the type of workpiece and the way it is clamped, the distance between the machine zero and workpiece zero can vary. In part program processing this is compensated for by the zero offset.
P - Tool setting point
W- Workpiece zero
F - Slide reference point
XMR, ZMR Reference point coordinates
XMW, ZMW Zero offset
M- Machine zero
R - Machine reference point
WR- Workpiece reference point

## Slide 19: CNC CONTROLLER OPERATING AREA (MACHINE)
Machine: This operating area is used for Execution of part programs, Manual control operation of machines. In this operating area we can see the different area of mode Operating areas, Channel status, Program status, Channel name, Alarm and message line, Operating mode, Program name of selected program, Channel operational messages, Channel status display, Additional explanatory text (Help) can be called, Working windows, NC displays The working windows (program editor) and NC displays (feedrate,tool) available in the selected operating area are displayed here, Dialog line with Operator prompts , Recall function, ETC. function, Horizontal softkeys, Vertical softkeys,. When press the "Area switchover" key, operating areas are displayed on the horizontal softkey bar and operating modes are displayed on the vertical softkey bar. By this key to go to the area menu bar from any location in the menu hierarchy if you wish to select another operating mode or a different operating area.

## Slide 20: CNC CONTROLLER OPERATING AREA (PARAMETER)
CNC system have many type of parameters which control the different function of machine.
Too Data, Tool Compensation, tool Management, Setting parameters, Zero Offsets,R-parameter
Machine parameter,Working Area Limitation
Setting Parameter: Setting parameter contains various setting data, Jog data, Spindle data, Dry run feed rate, Starting angle thread cutting,Zero Offsets, Setting bits, etc. Setting data are related with jog feed, dry run feed, Spindle max & min. speed, axes negative & positive limitation etc.
R-Parameter: This is programming parameter. R-parameter mainly used for arithmetic function in in part program .
Machine Parameter: Machine parameter is heart of CNC system. Without this parameter machine never work. M/c parameter contains various data like machine configuration data, Servo drive configuration data, Individual Axis data, Display data, Channel data,
Configuration data decide the no. of axes in CNC machine, which type of drive used in machine, rating of servo drives. Drive configuration data indicate the power of servo motor & drives, Its current capacity , torque, acceleration, Gain etc. Axis parameter contains the each individual axis parameter like axis traverse limit in both direction, type of measuring system, encoder pulse,

## Slide 21: BENEFITS OF CNC SYSTEM
INCREASED FLEXIBILITY.
IMPROVED QUALITY.
REDUCED LEAD-TIME.
HIGHER PRODUCTIVITY.
ECONOMICAL BATCH PRODUCTION.
REDUCED CYCLE-TIME.
REDUCED SCRAP GENERATION.

## Slide 22: PROGRAMMABLE LOGIC CONTROLLER
WHAT IS PLC ?
BASIC ELEMET OF PLC CONTROLLER
PLC PROGRAMMING
PLC LANGUAGES
PLC HARDWARE
BENEFITS OF PLC

## Slide 23: WHAT IS PLC ?
A programmable logic controller, PLC, or programmable controller is a small computer used for automation of real-world processes, such as control of machinery on factory assembly lines CNC machines . The PLC usually uses a microprocessor. The program is usually created by an engineers at an industrial site, rather than a professional computer programmer. The program is stored in battery-backed memory.
The main difference from other computers are the special input/output arrangements. These connect the PLC to a process's sensors and actuators. PLCs read limit switches, dual-level devices, temperature indicators and the positions of complex positioning systems. Some even use machine vision. On the actuator side, PLCs drive any kind of electric motor, pneumatic or hydraulic cylinders or diaphragms, magnetic relays or solenoids. The input/output arrangements may be built into a simple PLC, or the PLC may have external I/O modules attached to a proprietary computer network that plugs into the PLC.
PLCs were invented as less-expensive replacements for older automated systems that would use hundreds or thousands of relays and cam timers. Often, a single PLC can be programmed to replace thousands of relays. Programmable controllers were initially adopted by the automotive manufacturing industry, where software revision replaced the re-wiring of hard-wired control panels.

## Slide 24: BASIS ELEMENT OF PLC CONTROLLER

## Slide 25: PLC PROGRAMMING
PLCs programs are generally written in a special application on a personal computer then downloaded over a custom cable to the PLC. The program is typically stored in the PLC either in battery-backed-up RAM or some other non-volatile memory (flash).
PLC's were programmed in "ladder logic", which strongly resembles a schematic of relay logic. Modern PLCs can be programmed in a variety of ways, from ladder logic to more traditional programming languages such as BASIC and C. Another method is State Logic, a Very High Level Programming Language designed to program PLCs based on State Transition Diagrams.
Recently, the International standard IEC 61131-3 has become popular. IEC 61131-3 currently defines 5 programming languages for programmable control systems: FBD (Function Block Diagram), LD (Ladder Diagram), ST (Structured Text, Pascal type language), IL (Instruction List) and SFC (Sequential Function Chart). These techniques emphasize logical organization of operations.
Ladder logic is widely used to program industrial Programmable logic controllers, where sequential control of a process or manufacturing operation is required. Ladder logic is useful for simple but critical control systems, or for reworking old hardwired relay circuits. As programmable logic controllers became more sophisticated it has also been used in very complex automation systems

## Slide 26: PLC HARDWARE
PLC controller consist of CPU (Central processor
unit) ,PLC Input board, PLC Output board and
Power Supply board.
Power supply is used in bringing electrical
energy to central processing unit. Most PLC
controllers work either at 24 VDC or 220 VAC.
Main function of CPU is to process the PLC
program .In CPU board the PLC program is stored
in RAM. This program is backup by Battery. CPU
board contain microprocessor .
The main function of PLC Input board is to give the
input signal to CPU from sensor like limit switch,
proximity switch ,pressure switch, float switch,
Optical sensor etc.
The main function of PLC output board is to actuate
the actuator like relays, solenoid valves, contactor
etc. CPU generate the output signal according to PLC
program and this signal is outputted at output board.
The PLC program is written in Ladder logic ,STL and
CFB (control Function Block) language.

## Slide 27: BENEFITS OF PLC
Flexibility: One single Programmable Logic Controller can easily run many machines.
Correcting Errors: In old days, with wired relay-type panels, any program alterations required time for rewiring of panels and devices. With PLC control any change in circuit design or sequence is as simple as retyping the logic. Correcting errors in PLC is extremely short and cost effective.
Space Efficient: Today's Programmable Logic Control memory is getting bigger and bigger this means that we can generate more and more contacts, coils, timers, sequencers, counters and so on. We can have thousands of contact timers and counters in a single PLC. Imagine what it would be like to have so many things in one panel.
Low Cost: Prices of Programmable Logic Controlers vary from few hundreds to few thousands. This is nothing compared to the prices of the contact and coils and timers that you would pay to match the same things. Add to that the installation cost, the shipping cost and so on.
Testing: A Programmable Logic Control program can be tested and evaluated in a lab. The program can be tested, validated and corrected saving very valuable time.
Visual observation: When running a PLC program a visual operation can be seen on the screen. Hence troubleshooting a circuit is really quick, easy and simple.

## Slide 28: SERVO SYSTEM
SERVOMECHANISM
SERVO SYSTEM BLOCK DIAGRAM
SERVO DRIVE
THE CONCEPT OF A SERVO SYSTEM
DRIVE TYPES
SERVO MOTORS
SERVO MOTOR BENIFITS

## Slide 29: SERVO MECHANISM
Servomechanism, usually shortened to just servo, is a device used to provide mechanical control at a distance. The most common type of servo is that mentioned, which gives positional control. Servos are commonly electrical or partially electronic in nature, using an electric motor as the primary means of creating mechanical force, though other types that operate on hydraulic or magnetic principles are available. Usually, servos operate on the principle of negative feedback, where the control input is compared to the actual position of the mechanical system as measured by some sort of transducer (Tachogenerator or Encoder) at the output. Any difference between the actual and wanted values is amplified and used to drive the system in the direction necessary to reduce or eliminate the error. A whole science of this type of system has been developed, known as servo system .
Servos are found in many applications. Servos are used to operate the CNC machines , throttle of engines that use a cruise control. Fly-by-wire systems in aircraft use servos to actuate the control surfaces that control the aircraft.

## Slide 30: SERVO DRIVE
Servo can be described as follows. A command signal which is issued from the user's interface panel comes into the servo's "positioning controller". The positioning controller is the device which stores information about various jobs or tasks. It has been programmed to activate the motor/load, i.e. change speed/position. The signal then passes into the servo control or "amplifier" section. The servo control takes this low power level signal and increases, or amplifies, the power up to appropriate levels to actually result in movement of the servo motor/load.These low power level signals must be amplified: Higher voltage levels are needed to rotate the servo motor at appropriate higher speeds and higher current levels are required to provide torque to move heavier loads.This power is supplied to the servo control (amplifier) from the "power supply" which simply converts.AC power into the required DC level. It also supplies any low level voltage required for operation of integrated circuits.As power is applied onto the servo motor, the load begins to move desired speed and position changes.As the load moves, so does some other "device" move. This other "device" is either a tachometer,resolver or encoder (providing a signal which is "sent back" to the controller). This "feedback" signal is informing the positioning controller whether the motor is doing the proper job.
Feedback device are Analog Tachogenerator, Digital Tachogenerator, Absolute Encoder, Incremental Encoder , Resolvers.

## Slide 31: THE CONCEPT OF A SERVO SYSTEM

## Slide 32: DRIVE TYPES

## Slide 33: SERVO MOTORS
Servomotors – A motor with a "feedback" device. Electronic packages control speed and position accuracy.Servo motors are normally used for linear motion & rotary motion in machine tools application & automation industries.
Servomotors are mainly two types as AC or DC motors. Servo motor basically works in velocity feedback system. In servomotor the feedback device is known as Tachogenerator or Encoder.
Early servomotors were generally DC motors because the only type of control for large currents was through SCRs . As transistors became capable of controlling larger currents and switching the large currents at higher frequencies, the AC servomotor became used more often. Early servomotors were specifically designed for servo amplifiers. Today a class of motors is designed for applications that may use a servo amplifier or a variable-frequency controller, which means that a motor may be used in a servo system in one application, and used in a variable-frequency drive in another application.
Type of servomotor
DC Servomotor:
AC servomotor

## Slide 34: SERVO MOTOR BENIFITS
High intermittent torque
High torque to inertia ratio
High speeds
Work well for velocity control
Available in all sizes
High performance
Small size
Wide variety of components
with specialized controls

## Slide 35: CNC RETROFITTING
OBJECTIVE OF CNC RETROFITTING
FEATURE OF CNC RETROFITTING
ADVANTAGES OF RETROFITTING

## Slide 36: WHAT IS CNC RETROFITTING ?
OBJECTIVES
COST- EFFECTIVE MODERNISATION.
LARGE SIZE & COSTLIER AGEING MACHINE TOOLS NEED
NOT BE DISCARDED.
RETROFITTING IS A STEPPING STONE TO A FULL FLEDGED
CNC TECHNOLOGY.
FACTORS FOR SELECTION
GEOMETRIC ACCURACY.
SOUND MECHANICAL CONDITION.
AVAILABILITY OF SPACE ON THE MACHINE.

## Slide 37: ADVANTAGES OF CNC RETROFITTING
A NEW LEASE OF LIFE TO THE MACHINE TOOLS THROUGH
  COST EFFECTIVE MODERNISTION
CAPABILITY ENHANCEMENT
  ADDITION OF FACILITIES
  RESTORATION OF ACCURACIES
QUALITY IMPROVEMENT
  BETTER ACCURACY
PRODUCTIVITY ENHANCEMENT BY 100-200% By
  CYCLE TIME REDUCTION
  REDUCTION IN REWORK / REJECTION
  REDUCTION IN DOWN TIME
FLEXIBILITY OF OPERATION & PROGRAMING
CAPABILITY OF ON-LINE PROGRAMMING /MONITORING THROUGH LAN/ DNC

## Slide 38: MAINTENANCE MANAGEMENT
MAINTENANCE is an important part of the life-cycle of Machine Tools & Plants, and must be considered from the design stage through the end-of-life stage of the system. Maintenance covers two aspects of systems - operation and performance. Maintenance is generally performed in anticipation of, or in reaction to, a failure. Maintenance is performed to ensure or restore system performance to specified levels. Improperly performed or timed maintenance can exacerbate problems because of faulty parts, maintainer error, or decreased profits. A systematic and structured approach to system maintenance, starting during the design process, is necessary to ensure proper and cost-effective maintenance.

## Slide 39
THANK YOU