## Slide 1
Control of Boiler Operation using PLC – SCADA

## Slide 2
CONTENTS
Introduction
DRAWBACK OF CONVENTIONAL SYSTEM
CRITICAL CONTROL PARAMETERS IN BOILER
AUTOMATION
Electrical control with logic gates
Programmable Logic Controller
PLC Working
Manual control

## Slide 3
SCADA
Features of SCADA
SCADA Architecture
BOILER OPERATION
Boiler Operation Flowchart
ADVANTAGES
CONCLUSION
REFERENCES

## Slide 4
I. INTRODUCTION
Over the years the demand for high quality, greater efficiency and automated machines has increased in the industrial sector of power plants. Power plants require continuous monitoring and inspection at frequent intervals. There are possibilities of errors at measuring and various stages involved with human workers and also the lack of few features of microcontrollers. Thus this paper takes a sincere attempt to explain the advantages the companies will face by implementing automation into them.
The boiler control which is the most important part of any power plant, and its automation is the precise effort of this paper.

## Slide 5
In order to automate a power plant and minimize human intervention, there is a need to develop a SCADA (Supervisory Control and Data Acquisition) system that monitors the plant and helps reduce the errors caused by humans. While the SCADA is used to monitor the system, PLC (Programmable Logic Controller) is also used for the internal storage of instruction for the implementing function such as logic, sequencing, timing, counting and arithmetic to control through digital or analog input/ out put modules various types of machines processes.
Systems are used to monitor and control a plant or equipment in industries such as oil and gas refining, water and waste control and transportation.

## Slide 6
II. DRAWBACK OF CONVENTIONAL SYSTEM
Errors due to the involvement of humans in the data collection and processing using complicated mathematical expressions.
In the coding process of this implementation with micro-controller, it requires a fast and efficient processing which on the other part depends on the length and sub-routines of the coding process.

## Slide 7
III. CRITICAL CONTROL PARAMETERS IN
BOILER
A. Level Control
Steam Drum level, De-aerator level and hot well level
B. Pressure Control
Force draft pressure, Induced draft pressure, Steam drum pressure, De-aerator pressure, Turbine inlet steam pressure, balanced draft pressure
C. Flow Control
Air flow, Steam flow, Water flow
D. Temperature Control
Steam drum temperature, Underbed boiler temperature, Turbine inlet steam temperature, Flue gas temperature.

## Slide 8
IV. AUTOMATION
Delegation of Human Control to technical Equipment aimed to wards achieving.
Advantages
Higher productivity, Superior quality of end
product, Efficient usage of raw materials and
energy, Improved safety in working condition.
History of Control and Automation
1. Manual control
2. With Logic Gate
3. Electrical control with logic gates
4. PLC

## Slide 9
Manual Control
In this, the Control and Automation are done by
Manual Operations.
Drawbacks:
Human Errors subsequently affect quality of end
product.
Hard Wired Logic Control
Bulky and complex wiring,

## Slide 10
Electronics Control with Logic Gates
In this, Contactor and Relays together with timers
and counters were replaced with logic gates and
electronic timers in the control circuits.
Advantages
Reduced space requirements, energy saving, less
maintenance and hence greater reliability.
The Major Drawbacks
Implementation of changes in the control logic as
well as reducing the project lead- time was not
possible.

## Slide 11
Programmable Logic Controller
In this, instead of achieving desired control and
automation through physical wiring of control
devices, it is achieving through program say software.
Advantages
Reduced Space, Energy saving, Easy trouble shooting, Error diagnostics programmer, Economical, Greater life and reliability,

## Slide 12
How PLC works
Basics of a PLC function are continual scanning of a program. The scanning process involves three basic steps.
Step 1: Testing input status
First the PLC checks each of its input with intention to see which one has status on or off.
Step 2: Programming execution
Here a PLC executes a program instruction by instruction based on the program and based on the status of the input has obtained in the preceding step, and appropriate action is taken
Step 3: Checking and Correction of output status
Finally, a PLC checks up output signals and adjust it has needed.

## Slide 13
PLC Working
At the beginning of each cycle the CPU brings in all the field input signals from the input signals from the module and store into internal memory as process of input signal. This internal memory of CPU is called as process input image (PII). User program (Application) will be available in CPU program memory. Once PII is read, CPU pointer moves in ladder program from left to right and from top to bottom. CPU takes status of input from PII and processes all the rungs in the user program. The result of user program scan is stored in the internal memory of CPU. This internal memory is called process output image or PIQ. At the end of the program run i.e., at the end of scanning cycle, the CPU transfers the signal states in the process image output to the output module and further to the field control.

## Slide 14
I/O driver (SCADA) picks up PII and PIQ and transfers the image to database and this image is called driver image. This driver image available in SCADA database is used for graphical view of process monitoring from operator station (OS) in the central control room.

## Slide 15
V. SCADA
SCADA stands for Supervisory Control and Data Acquisition. As the name indicates, it is not a full control system, but rather focuses on the supervisory level [2].
What is SCADA? It is used to monitor and control plant or equipment. The control may be automatic or initiated by operator commands. The data acquisition is accomplished firstly by the RTU’s(Remote telemetry or terminal units) scanning the field inputs connected to the RTU (it may be also called a PLC – programmable logic controller.). This is usually at a fast rate. The central host will scan the PTU’s (usually at a slower rate). The data is processed to detect alarm conditions, and if an alarm is present, it will be displayed on special alarm lists.

## Slide 16
Features of SCADA
1. Dynamic process Graphic
2. Alarm summery
3. Alarm history
4. Real time trend
5. Historical time trend
6. Security
7. Data base connectivity
8. Device connectivity
9. Scripts
10. Recipe management

## Slide 17
SCADA Architecture
Hardware Architecture
Figure 1: Typical Hardware Architecture
Software Architecture
Figure 2: Generic Software Architecture

## Slide 18
VI. BOILER OPERATION
Water plays a major part in the generation of steam. Inlet water to the steam drum should be in purified form, for that, PH value of the water should be maintained, and stored in de-aerator tank. Feed water pump is switched ON by using feed water pump switch. The water from the de-aerator tank is allowed to pass through two parallel pipes. In one pump the flow rate is maintained at 130% and in another it is 5%. Thus the failure of any one pipe does not affect the boiler operation. The water is passed through economizer, thus the heat in the outgoing gases is recovered, by transferring its heat to the water. Then the heated water is made to flow through steam and water drum.

## Slide 19
In this, water should be maintained at least at 50%. For sensing water level we use PID controller in AB PLC. When the level is lesser than or greater than 50%, PID controller senses the level change and sends the appropriate control signal to the feed water valve 1 or valve 2. Thus, in spite of any changes in disturbance variable, the water level can be maintained at 50% by proper turning of PID controller.
Water in the water drum is maintained at more than 75%. This water is circulated back to steam and water drum, due to difference in temperature, high amount of steam is generated.
The generated steam temperature may be greater or lesser than the desired temperature. So depending on the situation the generated steam is then passed through primary heater followed by secondary heater. The secondary temperature is monitored.

## Slide 21
Boiler Operation Flowchart

## Slide 22
Fig.4, Flow chart of Boiler Operation

## Slide 23
VII. ADVANTAGES
High integrity, self-monitoring low level alarm for the automated steam boilers.
Reduces energy costs, Maintenance, noise and vibration and Improved Operations.
Calculates deviation between the expected and the measured data.
Reduces plant fuel costs.
Early detection of degradation possible.
Provides the maximum flexibility in reconfiguring or dynamically modifying system parameters even during system operation.
Alarm is generated if computed value deviates from the process value by more than a specified interval.

## Slide 24
VIII. CONCLUSION
This paper presented here has kept in mind, the ceaseless changes that are relentlessly taking place in the contemporary scenario of the industrial segment. Emphasis has been given to the automation process that is now rapidly taking its place in all the power plants across the globe. The Paper has furnished itself to study the integral parts of the entire process involved, their implementation and the problems that may show up have also been given their due importance. The future work deals with the purification of water to the boiler and the air circulation for the boiler to burn the fuel using same automation technique.

## Slide 25
CONCLUSION

## Slide 26
IX. REFERENCES
Boyer, Stuart, A. SCADA: Supervisory Control and Data Acquisition, Instrument Society of America.
Ezell, Barry, “Supervisory Control and Data Acquisition Systems for Water Supply and Its Vulnerability to Cyber Risks” available on the internet at: http://watt.seas.virginia.edu/~bce4k/home.html.
Rockwell Automation SCADA System Selection guide Allen-Bradley, Publication AG-2.1. 1998.
Knight. U. “The Power System and its Operational and Control Infrastructure in emergencies” from contingency planning to crisis management.
Analysis of Fault-Tolerant systems, “IEEE transactions on Computers”, vol.38, No.6, 1989.